规 格 书

# SPECIFICATION

DESIGNATION   系　 列：SLIDE SWITCH

MODULE  NO   型　 号：HR-1101A

RATING           额 定 值：1A  250V  AC   /2A  125V AC

1.  CIRCUTT    回　 路：OFF-ON

2.  IMING      切换类型：NON-SHORTING

3.  STANDARD TEST CONDTTIONS SHALL BE 5 TO 35℃ IN TEMPERATURE AND 45 TO 85% IN HUMIDITY。

温度5-35℃,湿度45-85%标准状态下测试.

4.OPERATING TEMPERE RANGE—15 TO 65℃。

温度-15~65℃环境内使用. 保存温度-30~80℃

| 5. ELECTRICAL PERFORMANCE （电气性能） |
| --- |
| 5.1 | ITEM 项目 | TEST CONDISTION测试条件 | PERFORMANCE规格 |
|  | CONTACT RESISTANCE 接触阻抗 | Being measured at 1kHz small current(100mA Or less)Contact resistance meter. 在1kHz,100mA或以下小电流下测量. | 100mΩ max 100毫欧 以下 |
| 5.2 | INSULATION RESISTANCE 绝缘阻抗 | Measurements shall be made following Application of DC 500V potential Across terminals and across terminals And frame for 1 minute. 在端子之间和端子与壳之间加DC 500V 条件下,持续1分钟测量. | 100MΩmin. 100兆欧 以上. |
| 5.3 | WITHSTAND VOLTAGE 耐电压 | AC 500V (50Hz or 60Hz) shall be Applied across terminals and across terminals And frame for 1 minute. 在端子之间和端子与壳之间AC 500V(50Hz或60Hz) ,0.5mA电流条件下,持续1分钟测量. | There shall be no breakdown. 无击穿现象出现. |
| 6.MECHANICAL PERFORMANCE 机械性能 |
| 6.1 | ITEM 项目 | TEST CONDISTION测试条件 | PERFORMANCE规格 |
|  | OPERATING FORCE 动作力 | Measure at the point 3mm from the tip Of the actuator (knob). 在距离推杆前端3mm作测定点. | OFF-ON:180-450 gf |
| 6.2 | TERMINAL STRENGTH 端子强度 | A static force of 500gf being applied In one direction on the tip or the Terminal for 1 minute. 一个500gf力度施加于端子顶部的一个方向持续1分钟. | There shall be no sign of damage mechanically and electrically. 无任何机械损坏及电气性能损坏迹象. |
| 6.3 | ACTUATOR STRENGTH 推杆强度 | A static load of 1Kgf being applied In one direction of actuator for one min 一个1Kgf力度施加于推杆之一个方向持续1分钟。 | The deformation shall not be extreme and the actuator shall mechanically work normally. 推杆无变形,可以正常操作. |
| 7. ELECTRICAL PERFORMANCE （电气性能） |
| 7.1 | ITEM 项目 | TEST CONDISTION测试条件 | PERFORMANCE规格 |
|  | SLLDERING TEST 可焊性试验 | The tip of the terminals shall be dipped 2mm in the solder bath at a Temperatureof 260±5℃ for 3sec . 端子顶部被浸入焊锡池2mm深,温度350±5℃时间3秒. | A new uniform coating of solder Shall cover a minimum of 90% of the surface being immersed. 浸入的部分90%以上表面将被锡覆盖。 |
| 7.2 | RESISTANCE TO SOLDERING HEAT TEST 耐焊性试验 | Solder bath method Solder temperature 245±5℃ Immersion time 3±0.5scc Immersion depth up to the surface of the board Thickness of PCB 1.6 mm. 焊炉焊的温度控制在245±5℃，过炉焊接的时间3±0.5秒，于(基板)厚度为1.6 mm. Solder bath method Bit temperature 350±10℃ application time 3±0.5scc however excessive pressure shall not be applied to the terminal. 手焊接的时候温度需控制在360±10℃，时间为 3±0.5秒，但不能在排脚上施加异常压力。 | Without deformation of case Or excessive looseness of mechanically electrical characteristics Shall be satisfied. 本体无变形，能满足于机械、电器性能。 |
| 7.3 | LIFI TEST 寿命试验 | 10000cycles of operation at a rate of 15-18 cycles per minute with unloading. 无负载条件下,每分钟15-18次的速度操作10000次. | Contact resistance 接触阻抗. 150mΩ max.150毫欧以下. Operating force 动作力. ±30%Inltial value. 变化范围初始值30%. (3)ITEN 项目—5.2 (4)ITEN 项目—5.3 (5)ITEN 项目—6.2 (6)ITEN 项目—6.3 其它，皆满足机械、电气性能。 |
| 7.4 | HEAT TEST 耐热试验 | 85±10℃ for 96 hours , caner test keep in normal condition for 60minutes. 在85±10℃环境中放96小时,再放在正常环境中 60分钟后进行测试. | (1)Contact resistance 150mΩ max. 接触电阻150毫欧以下. (2)Insulation resistance 绝缘电阻. 50MΩmin 50兆欧以上. (3)There shall be no sign of damage mechanically and electrically. 无任何机械损坏及电器性能损坏迹象. |
| 7.5 | HUMIDITY TEST 耐湿试验 | 40±2℃ 90-95%RH for 96firs after test keep in mortal condition for 30 min. 在40±2℃ 90-95%RH环境中放96小时,再放在正常环境中,60分钟后进行测试. |  |
| 7.6 | COLD TEST 耐冷试验 | At -25±3℃ for 96hours,after test kept in normal condition for 60 min. 在-25±3℃ 环境中放96小时,再置于正常环境中,60分钟后进行测试 . |  |
| 7.7 | TEMPERATURE CYCELING TEST 温度交 变实 验 | In FIG. for 5 cycles after lest Keep in normal condition for 30 min.In FIG .For5 cycles,after test Keep in normal condition for 30 min. 如图示之环境中，循环5次后，再置于正常环境中，30分钟后，进行测试。 |  |
| 8．MATERIAL SPECIFICATIONS 材料规格 |
| NO. | PARTS零部件 | MATERIAL 材料 | FINISH表面状态 |
| 1 | LOWER COVER 下盖 | PC+ABS | BLACK 黑色 |
| 2 | LOAM CAKE 上盖 | PC+ABS | BLACK 黑色 |
| 3 | KNOB 拨块 | PC+ABS | BLACK 黑色 |
| 4 | TERMINAL1 端子1 | BRASS STRIP 铜带 | NI PLATED 镀镍 |
| 5 | TERMINAL 端子 | BRASS STRIP 铜带 | NATURAL 自然（清洗） |
| 6 | CONTACT CHIP 接触片 | BRASS STRIP 铜带 | NI PLATED 镀镍 |